# T-CLOCK Inspection Worksheet

T-CLOCK is a mnemonic developed by the Motorcycle Safety Foundation for assisting you in doing a comprehensive pre-ride (or a pre-purchase) inspection of a motorcycle. It is easily memorized and very useful. The individual letters stand for the specific areas to check:

- T — Tires & Wheels

- C — Controls

- L — Lights

- O — Oil

- C — Chassis

- K — Kickstand

Just print these pages and stick them on the wall near where you store your mototcycle(s), or stuff them in your tank bag or under the seat...

| T — TIRES & WHEELS |
| --- |
| Item | Check | Look for | Check off |
| Tires | Condition | Tread depth, wear, weathering, evenly seated, bulges, imbedded objects. | Front - Rear |
|  | Air Pressure | Check when cold, adjust to load/speed. | Front - Rear |
| Wheels | Spokes | Bent, broken, missing, tension, check at top of wheel: "ring" == OK, "thud" == loose spoke. | Front - Rear |
|  | Cast | Cracks, dents. | Front - Rear |
|  | Rims | Out of round/true == 5mm. Spin wheel, index against a stationary pointer. | Front - Rear |
|  | Bearings | Grab top and bottom of tire and flex: No freeplay (click) between hub and axle, no growl when spinning | Front - Rear |
|  | Seals | Cracked, cut or torn, excessive grease on outside, reddish-brown outside. | Front - Rear |

| C — CONTROLS |
| --- |
| Item | Check | Look for | Check off |
| Levers | Condition | Broken, bent, cracked, mounts tight, ball ends on handlebar lever. | Front - Rear |
|  | Pivots | Lubricated. |  |
| Cables | Condition | Fraying, kinks, lubrication; ends and length |  |
|  | Routing | No interference or pulling at steering head, suspension; no sharp angles, wire looms in place. |  |
| Hoses | Condition | Cuts, cracks, leaks, bulges, chafing, deterioration. |  |
|  | Routing | No interference or pulling at steering head, suspension, no sharp angles, wire looms in place. |  |
| Throttle | Operation | Moves freely, snaps closed, no revving. |  |

| L — LIGHTS |
| --- |
| Item | Check | Look for | Check off |
| Battery | Condition | Terminals clean and tight, electrolyte level, held down securely. |  |
|  | Vent Tube | Not kinked, routed properly, not plugged. |  |
| Lenses | Condition | Cracked, broken, securely mounted, excessive condensation. |  |
| Reflectors | Condition | Cracked, broken, securely mounted. |  |
| Wiring | Condition | Fraying, chafing, insulation. |  |
|  | Routing | Pinched, no interference or pulling at steering head or suspension, wire looms and ties in place, connectors tight, clean. |  |
| Headlamp | Condition | Cracks, reflector, mounting and adjustment system. |  |
|  | Aim | Height and right/left. |  |

| O — OIL |
| --- |
| Item | Check | Look for | Check off |
| Levels | Engine Oil | Check warm on centerstand, dipstick, sightglass. |  |
|  | Hypoid Gear Oil | Transmission, rear drive, shaft. |  |
|  | Hydraulic Fluid | Brakes, clutch, reservior or sight glass. |  |
|  | Coolant | Reservoir and/or coolant recovery tank — cool only. |  |
|  | Fuel | Tank or guage. |  |
| Leaks | Engine Oil | Gaskets, housings, seals. |  |
|  | Hypoid Gear | Gaskets, seals, breathers. |  |
|  | Hydraulic Fluid | Hoses, master cylinders, calipers. |  |
|  | Coolant | Radiator, hoses, tanks, fittings, pipes. |  |
|  | Fuel | Lines, fuel taps, carbs. |  |

| C — CHASSIS |
| --- |
| Item | Check | Look for | Check off |
| Frame | Condition | Cracks at gussets, accessory mounts, look for paint lifting. |  |
|  | Steering-Head Bearings | No Detent or tight spots through full travel, raise front wheel, check for play by pushing/pulling forks. |  |
|  | Swingarm Bushings/Bearings | Raise rear wheel, check for play by pushing/pulling swingarm. |  |
| Suspension | Forks | Smooth travel, equal air pressure/damping and anti-dive settings. |  |
|  | Shock(s) | Smooth travel, equal preload, air-pressure and damping settings, linkage moves freely and is lubricated. |  |
| Chain/belt | Tension | Check at tightest point. |  |
|  | Lubrication | Side plates when hot. Note: do not lubricate belts! |  |
|  | Sprockets | Teeth not hooked, securely mounted. |  |
| Fastners | Threaded | Tight, missing bolts, nuts. |  |
|  | Clips | Broken, missing. |  |
|  | Cotter Pins | Broken, missing. |  |

| K — KICKSTAND |
| --- |
| Item | Check | Look for | Check off |
| Centerstand | Condition | Cracks, bent. |  |
|  | Retention | Springs in place, tension to hold position. |  |
| Sidestand | Condition | Cracks, bent (safety cut-out switch/pad if equipped). |  |
|  | Retention | Springs in place, tension to hold position. |  |